## Slide 1
Transport of Nuclear Material and Products
Mr. Trevor Dixon
World Nuclear Transport Institute

## Slide 2: Presentation
Radioactive material
Regulatory regime
Uses of radioactive material
Nuclear fuel cycle material
Packaging integrity
Conclusions

## Slide 3: Radioactive Material
Results from an atom with too many or too few neutrons in the nucleus
Unstable atoms seek to become stable by emitting energy as Alpha, Beta, Gamma or Neutron radiation
Alpha
Beta
Gamma

## Slide 4: Uses of Radioactive Material
Nuclear Energy
Industry & Agriculture
Medicine &
Research
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5
Putting Radioactive Material in Perspective
The US “Priority List of Hazardous Substances”
comprises 275 substances
The highest ranking, radioactive material on list is
Uranium at position 92
Those materials ranked higher than Uranium
include; Arsenic (1), Lead (2), Vinyl Chloride (4),
Cyanide (26), Methane (65), Chlorine (84) and Asbestos (90).
Cobalt 60 , Plutonium 239 are ranked 126th, 130th
respectively.
Notes: <number>
<footer>
<header>
<date/time>
“The (US) Comprehensive Environmental Response ,Compensation and Liability Act (CERCLA) Section 104 (I), requires the Agency for Toxic Substances and Disease Registry (ATSDR) and the US Environmental Protection Agency (EPA) to revise the Priority List of Hazardous Substances periodically to reflect additional information on hazardous substances. The CERCLA priority list is revised and published on a two year basis, with a yearly informal review and revision.
These substances pose the most significant potential threat to human health due to their known or suspected toxicity for human exposure and are found on the National Priorities List (NPL).
Each substance on the CERCLA list is a candidate to become the subject of a toxicological profile prepared by ATSDR and subsequently a candidate for the identification of priority data needs. The priority list is based on an algorithm that utilizes the following three components: frequency of occurrence at NPL sites, toxicity and potential for human exposure to the substances found at NPL sites. This algorithm utilizes data from ATSDR’s HazDat database, which contains information from ATSDR’s public health assessments and health consultations ”
Extracted from “Hazardous Technical Information Services, Mar-April 2001” and from “ATSDR-1999 CERCLA List of Priority Hazardous Substances”
http://www.atsdr.cdc.gov

## Slide 6
Nuclear power supplies nearly 16% of world electricity
Increasingly important to meet growing demand, within environmental and economic constraints
Safe, efficient and reliable international transports of nuclear fuel cycle materials are vital to sustain this industry
In over 40 years, there has never been a significant radiological consequence resulting from the transport of nuclear materials
Nuclear Power

## Slide 7
The Nuclear Fuel Cycle – Reprocessing Option

## Slide 8
Design Standards for Nuclear Fuel Cycle Packages
Basis is the IAEA Regulations
Underlying philosophy is that safety is vested principally in the package
Four types of package for surface transport (Excepted, Industrial, Type A, Type B) depending on activity and physical form of material
Type C for air transport of higher activity materials
Regulations define design standards and appropriate tests for each

## Slide 13: Basic Principle Regarding Radioactive Material Transport Packages
EITHER
- OR -
RESTRICT THE TYPE AND ACTIVITY OF THE RADIOACTIVE CONTENTS
PROVIDE SEVERE ACCIDENT PROOF PACKAGE DESIGN
Safety is provided by graded approach to package design
Notes: <number>
<footer>
<header>
<date/time>
Key Points:
This is a critical slide. Explain that type of package to be used is dependent on the content therein. If the contents can be limited, less restrictive package is required. If content cannot be limited (e.g., >A1 or A2), accident proof packaging is required.
(NOTE: This slide contains the philosophy used in establishing the regulations for the safe transport of radioactive material. See “Key Points”, Slide #6.)
The first 5 PACKAGE types listed in § 230 (Excepted, IP-1, IP-2, IP-3 and A are only designed and tested to withstand routine and normal conditions of transport (§106 TS-R-1).
Consequently their RADIOACTIVE CONTENTS are restricted so that any losses under accident conditions will present no significant hazard to workers or the general public.
An EXCEPTED PACKAGE can carry only limited quantities of radioactive material as described in TABLE III of TS-R-1. In addition the surface dose rates from EXCEPTED PACKAGES must not exceed 0,005 mSv per hour.
The INDUSTRIAL PACKAGES TYPE IP-1, IP-2 and IP-3 are only designed and tested to carry qualified RADIOACTIVE CONTENTS. These qualified contents are the low specific activity materials or surface contaminated objects LSA I, LSA II, LSA III, SCO I, or SCO II as defined in §226 or §241 of the regulations.
A TYPE A PACKAGE is restricted to carry RADIOACTIVE CONTENTS up to a maximum activity of A1 or A2 TBq. The values of A1 or A2 are nuclide dependent and most relevant values are given in TABLE I of TS-R-1. Default values are provided in TABLE II of TS-R-1 for unknown nuclides or mixtures.
Objective(s):
Obj 2 and 5
References:
Course materials
Exercises:
None

## Slide 14: The Scope of the Transport Regulations
A graded approach to performance standards with 3 severity levels is used
  Routine conditions of transport (incident free)
  Normal conditions of transport (minor mishaps)
  Accident conditions of transport
The extent of performance standards increases as the potential hazard of the radioactive material contents increases
Notes: <number>
<footer>
<header>
<date/time>

## Slide 15
Regulatory Tests for Type B Packages
Mechanical tests to assess impact and penetration resistance, including a 9 metre drop onto an unyielding surface
Thermal test in a fully engulfing 8000 C fire for 30 minutes
Water immersion test up to a depth of 200 metres
These are severe tests which cover situations which can be realistically envisaged in transport
Do other dangerous goods packaging under go such test?

## Slide 18
100 mph crash demonstration Do they do this with any other packages?

## Slide 19
Or this? At 165 km/h

## Slide 20
Conclusions
IAEA Regulations provide a sound basis for the safe transport of nuclear fuel cycle materials
On this basis international transport has been operated safely and efficiently for over 40 years
In the last forty years of transporting nuclear material around the world there has been no incident which has resulted in significant radiological damage to man or the environment.
Thank You.